## Slide 1: Respiratory Protection & Silica Awareness
OSHA 29CFR 1926.103 (1910.134)

## Slide 2: HOW TO REDUCE YOUR RISK
ENGINEERING CONTROLS
  Physically Moving the Hazard
  Enclose the Hazard so it’s Not exposed
  Establish Barriers/Ventilate to Minimize Exposure
ADMINISTRATIVE CONTROLS
  Necessary Precautions
  Site Specific Work Plans

## Slide 3
Why do People Continue to Make Choices Proven to Severely Injury & Kill Themselves?

## Slide 4: 3 Most Common Reasons for Bad Choices
PERCEPTIONS
HABITS
BARRIERS

## Slide 5: WHY ARE WE HERE TODAY?
Respiratory Protection &
Silica Standard Awareness…..

## Slide 6
ENGAGEMENT OF THE PLAN DOES NOT REQUIRE ENFORCEMENT OF THE PLAN…….

## Slide 7: THE STUFF WE DEAL WITH OUT THERE
DUSTS
  Grinding
  Crushing
  Sanding
  Sawing
MISTS/VAPORS
  Spraying
  Cleaning
  Solvents
  Volatile Compounds
FUMES
  Molten Metal
  Welding
  Laser Cutting
GASES
  Oxygen
  Carbon Dioxide
  Carbon Monoxide
  Hydrogen Sulfide

## Slide 8: N100 USE
MANDATORY MINIMUM USE IF DRY CUTTING, DRILLING WITH CONRETE
VOLUNTARY USE FORM APPENDIX D
DO NOT USE WHEN WORKING WITH GASES, VAPORS, ASBESTOS, OR WHEN PARTICULATES EXCEED 10X OSHA PEL (Permissible Exposure Limits)
Assigned Protection Factor (APF10)
DO NOT USE IN IDLH ATMOSPHERES OR OXYGEN DEFICIENT AREAS

## Slide 9: Mandatory Employee Information: Voluntary Use
Appendix D – 29 CFR 1910.134
Please Read This Document
Any Questions??

## Slide 10: FACIAL HAIR
Employees must be clean shaven in order to have respirators properly fitted for use.

## Slide 11
AUTHORIZED USE ONLY!
  If you have to ask if you are qualified to wear, you probably aren’t qualified to wear a respirator.
DO NOT BRING YOUR OWN RESPIRTATORS

## Slide 12: Standard Respiratory Program
Online Medical Exam
  3M Questionnaire
  Determines Eligibility Based on Health Inquiry
  Follow-up Physical with Medical Dr. may be Necessary
PowerPoint Presentation
  Review of PSC Standards
  OSHA Requirement
Respirator Fit Test
  Bitrex “Smoke” Test

## Slide 13: Silica Awareness Standard
Based on the personal air monitoring results as well as observations that were made during the collection of the above exposure assessment-based data, following are reasonable conclusions that can be made:
The testing results indicate that the employee’s calculated 8-hour exposure to quartz silica for these cutting scenarios would not have exceeded 1/10th of the calculated quartz silica exposure limit.
The testing results indicate that the dry-cutting of asphalt emitted concentrations of quartz silica that are nearly twice than the dry-cutting of concrete.
The testing results indicate that the wet-cutting systems for both the Stihl and Norton pavement cutting devices were effective at minimizing the emission of airborne pavement-based particulates.
The moderate amount of dust that is emitted during the dry cutting of concrete and asphalt creates a potential for other employees in the immediate work area to be exposed to such airborne particulates.

## Slide 14: Concrete or Asphalt Cutting Recommendations
Whenever possible, the wet-cutting method should be utilized for both the hand-held Stihl and push-style Norton pavement cutting systems.
All employees should be instructed of their need to take the necessary precautions to position the hand-held and the push-style pavement cutting saws in a manner which minimizes their exposure to airborne particulates that are generated during dry cutting activities. Based on observations that were made during this monitoring, this would involve pointing the saw into the wind for the Stihl hand-held saw and traveling with the wind with the Norton push-style saw.
The use of approved negative-type respiratory protection during the dry cutting of concrete asphalt would be acceptable provided that additional forms of particulate exposure are not present during the remainder of the employee’s work shift.
In order to maximize the protection that worn respirators provide, it is recommended that all employees who are required to wear approved respiratory protection also be required to be clean shaven at the beginning of each work-day.

## Slide 15: OSHA Silica Standard 1926.1153
Focuses on:
  a < or > 4 hour threshold
  Indoor/Outdoor
  Wet or Dry Operations
For ALL WET OPERATIONS OUTSIDE UNDER 4 Hours, NO MASK REQUIRED.
Walk-Behind Saws: As long as use is OUTDOORS and WET METHODS performed: NO MASK REQUIRED <>4Hrs
Hand-Held Saws: When Used OUTDOORS & WET METHODS performed: < 4hrs NO MASK; >4hrs N100
Jackhammer/Chippers: When used OUTDOORS & WET METHODS performed: < 4hrs NO MASK; >4hrs N100
Hand/Stand Drilling: When used OUTDOORS & when dust collection performed: NO MASK REQUIRED <>4Hrs
ANY DRY METHODS or INDOOR USE MUST USE N100

## Slide 23: LUNG X-RAY
This is a picture of a healthy lung x-ray. Note the clarity of the lung areas. There appear to be no defects, marks or abnormalities here. This is what we want to see on our x-rays.

## Slide 24: SILICOSIS
Shortness of breath exacerbated by exertion
Cough, often persistent, sometimes severe
Fatigue
Tachypnea (rapid breathing), often labored
Loss of appetite and weight loss
Chest pain
Fever
Gradual dark shallow rifts in nails eventually leading to cracks as protein fibers within nail beds are destroyed.
In advanced cases, the following may also occur:
Cyanosis (blue skin)
Cor pulmonale (right ventricle heart disease)
Respiratory insufficiency